Hardware Part of the project:

Smart sensing for energy monitoring system for industrial refrigeration facilities comes with various sensors as part of the capstone project. We have included several sensors which are described below.

### 1. Thermal Camera:
It is also called Thermographic camera or Infrared camera which create images using infrared radiation. In this project we will be using this sensor to measure the temperature of the items which enters in the refrigeration area from the truck. This way we can save the time and the manpower at the same time.
 In our capstone project we are going to use Grove – Thermal imaging camera/ IR Thermal sensor Array 32x24 (MLX90640). The camera can preset dynamic thermal images and detect temperature from -40*C to 300*C. It has 32x24 Array of thermal sensors. It has accuracy of ±1.5*C. It can measure the temperature from feet away.
The module can be interfaced with MCU with I2C protocol. However, the official website says that we can not interface this sensor with Arduino Uno because of not enough RAM.(seeed, n.d.)

Good resolution cameras with large arrays can not be interfaced with Arduino Uno because of it’s lower calculating capabilities. In order to get the data from good quality temperature camera, we will have to use wifi module.(Spasov et al., 2019, #).
https://github.com/Seeed-Studio/Seeed_Arduino_MLX9064x#seeed-arduino-mlx90640--

# Referance:

seeed. (n.d.). Grove - Thermal Imaging Camera / IR Array MLX90640 110 degree. seeed. https://www.seeedstudio.com/Grove-Thermal-Imaging-Camera-IR-Array-MLX90640-110-degree-p-4334.html
Spasov, G. V., Tsvetkov, V., & Petyrova, G. (2019, September). Using IR array MLX90640 to build an IoT solution for ALL and security smart systems. https://www.researchgate.net/publication/336786254_Using_IR_array_MLX90640_to_build_an_IoT_solution_for_ALL_and_security_smart_systems